## Slide 1
BOTSWANA INTERNATIONAL UNIVERSITY OF SCIENCE AND TECHNOLOGY
Department of Electrical, Computer and Telecommunications Engineering
Adaptive Multi-Agent Reinforcement Learning for Traffic Signal Optimisation along the Palapye A1 Urban Corridor
Tsotlhe Nayang Seiphepi | Student ID: 21001137
Supervisor: Dr Bokamoso Basutli
EEEN510 Final Year Project | 2025

## Slide 2
Presentation Outline
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
1. Introduction & Problem
2. Research Objectives
3. System Architecture
4. Phase 1 SA-PPO Results
5. Phase 2 MAPPO Design
6. MAPPO Training
7. Evaluation Results
8. Conclusions & Future Work
A two-phase project — from single-agent PPO at one junction to cooperative MAPPO across the full A1 corridor.

## Slide 3
Introduction — Why Palapye?
The problem that motivates this project
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
• Palapye: key transit hub on the A1 highway between Gaborone and Francistown
• Rapid commercial and population growth — Morupule Coal Mine, BIUST campus activity
• Existing signal infrastructure relies on static, pre-timed fixed cycles
• Fixed-time control is blind to queue lengths and cannot adapt to peak demand
• Consequences: chronic congestion, excessive idling, elevated fuel use and emissions
• Three closely spaced signalised junctions within ~1 km — decisions at one affect the others
Problem Statement
Urban intersections in Palapye experience chronic congestion and inefficient traffic flow due to fixed-time controllers that cannot adapt to real-time conditions, coordinate across junctions, or respond to varying demand.
Research Gap
• No adaptive / RL controller has been deployed or evaluated on a Botswana signalised network
• No publicly available traffic count dataset for Palapye intersections

## Slide 4
Research Objectives & Contributions
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Four Objectives
• YOLOv8 vehicle detection module validated on Palapye footage
• SUMO three-intersection A1 corridor model with 6 demand scenarios
• MAPPO with Centralised Training, Decentralised Execution (CTDE) for 3 cooperative agents
• Quantitative comparison: MAPPO vs SA-PPO vs Fixed-Time across all scenarios
Key Contributions
• First cooperative MARL controller on a real Botswana road network
• Reusable SUMO simulation environment — generates training data for future researchers
• First quantitative Fixed vs SA-PPO vs MAPPO comparison at the A1 corridor
• YOLOv8 pipeline providing a real-world sensing pathway
Two-Phase Progression
Phase 1
Single-Agent PPO
1 junction · 1 demand scenario Stable-Baselines3 · ~5M steps
↓ extends to
Phase 2
MAPPO CTDE
3 junctions · 6 scenarios · curriculum Custom MAPPO · 1.5M steps

## Slide 5
System Architecture
From camera sensing to adaptive signal control
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Camera / YOLOv8 Vehicle Detection
→
Traffic State Extraction (queue, wait, speed)
→
RL Controller Policy Decision (PPO / MAPPO)
→
SUMO + TraCI Signal Actuation (phase command)
→
Performance Metrics (delay, throughput, pressure)
↺ feedback loop: performance metrics drive next policy update
SUMO Network
Real Palapye A1 geometry 3 signalised junctions 6 demand scenarios Step-length: 3 s
MAPPO CTDE
Shared Actor (22-dim obs per agent) Centralised Critic (66-dim joint state) Cooperative reward (global waiting time) 3 agents, parameter sharing
YOLOv8 Module
Anchor-free detection head Validated on Palapye footage Queue length estimation Future: integrate into SUMO loop

## Slide 6
Phase 1: Single-Agent PPO vs Fixed-Time
Single intersection | 9,000 simulation timesteps | 5 demand phases
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Throughput
+48.5%
p < 0.001 | d = 0.156
Queue Length
−27.8%
p < 0.001 | d = 0.253
Traffic Pressure
−27.3%
p < 0.001 | d = 0.239
Delay (aggregate)
−10.1%
Negligible | d = 0.131
Stop Ratio
−3.6%
p = 0.017 | d = 0.042
PPO achieved statistically significant improvements in the three highest-value metrics. Delay aggregate is misleading — phase-specific analysis shows 50–68% improvement during heavy and peak demand.
Demand Phase
Delay improv.
Queue improv.
Throughput improv.
Light (0–60 s)
+64.8%
−1.5%
+—
Heavy (120–180 s)
+68.2%
+100%
+100%
Peak (180–240 s)
+50.1%
−34.4%
−20.9%
Extended (300 s+)
−11.7%
+29.9%
+39.8%
Training: ~5M steps | Stable-Baselines3 PPO | Reward converged at −230 around 600k steps

## Slide 7
Phase 2: MAPPO System Design
Centralised Training, Decentralised Execution — 3 cooperative agents
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Why MAPPO?
• Single-agent PPO has no cross-junction visibility — cannot anticipate spillback
• Fixed-time controller cycles blindly regardless of queue state
• MAPPO: each agent observes its own 22-dim local state for execution...
• ...but a centralised critic sees the full 66-dim joint state during training
• Global cooperative reward aligns agents toward minimising network-wide waiting time
• Green wave pre-computation biases agents toward coordinated platoon release
• 3-stage curriculum: simple → moderate → all 6 scenarios
Observation (22 dims per agent):
Queue counts (incoming/outgoing) • Waiting time per lane • Stop ratio • Current phase one-hot • Phase timer • Green-wave offset signal
Action space: Discrete(3) — 3 green phase configurations per junction
Local Obs o₁ (22-dim)
Local Obs o₂ (22-dim)
Local Obs o₃ (22-dim)
Shared Actor πθ
Centralised Critic Vϕ (joint state 66-dim)
Training Only ↓
Execution Only ↓

## Slide 8
MAPPO Training Setup & Demand Scenarios
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Training Hyperparameters
Total timesteps
1,500,000
Parallel environments
4
Episode length
500 steps × 3 s = 25 min sim
PPO clip ε
0.2
GAE λ / discount γ
0.95 / 0.99
Learning rate
3×10⁻⁴ (Adam)
Entropy coefficient
0.01
Training hardware
Intel Core i7 CPU, 16 GB RAM
Approx. training time
3–4 hours (CPU-only)
6 Demand Scenarios (curriculum rotation)
low
Off-peak, minimal vehicles
normal
Average daily flow
rush_hour_am
Morning rush inbound
rush_hour_pm
Evening rush outbound
holiday
Heavy through-traffic, few turns
incident
Partial closure, asymmetric demand
3-Stage Curriculum
• Stage 1 — low + normal (simple demand; establishes queue-clearing behaviour)
• Stage 2 — adds rush_hour_am / rush_hour_pm (moderate congestion; learns phase extension)
• Stage 3 — all 6 scenarios including holiday + incident (full demand diversity)
Reward: r = −Σ tanh(wait_i / (n_lanes · 60)) across all 3 junctions (cooperative signal)

## Slide 9
MAPPO Training Convergence
1.5 million environment steps — key diagnostic curves
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Mean Training Reward
Starts −15, rises steeply to −11 by 200k steps, plateaus near −9 from 1M steps onward. Residual oscillations = multi-agent non-stationarity.
Evaluation Reward (most important)
Rises from −9 → near −2 by 1.5M steps. 78% reduction in evaluation penalty. Clean plateau beyond 1M steps confirms stable, generalisable cooperative policy.
Critic Loss
Starts at 4.5 (uninitialised critic). Drops sharply to ~1.5 as critic fits returns. Stabilises at 1.4–1.6 — prerequisite for reliable advantage estimation.
Policy Entropy
Begins near 0.95 (near-uniform over phases). Decreases to ~0.3 at convergence. Retains residual entropy: confident but not collapsed — healthy MAPPO profile.
All curves shown with exponential smoothing to reveal trend; raw signals retained as supplementary evidence.
Actor Loss Arc
Actor loss begins near −0.004, rises to −0.002 mid-training (large gradients as policy moves away from random init), then decreases to −0.003 as PPO clipping activates less often and updates become conservative. No sharp spikes or sign changes confirm the clipping prevented any destabilising update.
Overall: clean convergence with cooperative policy emerging around 400k–800k steps.
The evaluation reward plateau at −2 (vs −9 at start) is the key evidence that MAPPO learned a stable, generalisable cooperative policy across all six demand scenarios.

## Slide 10
MAPPO Evaluation Results — Waiting Time & Queue Length
Measured exclusively at TL_A (junction 6073919354) across all 6 scenarios | n=3 episodes per cell
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Mean Waiting Time per Lane (s) at TL_A
Scenario
MAPPO
Fixed-Time
Random
MAPPO vs Fixed
low
0.06
0.97
0.92
−94.3%
normal
0.19
2.18
1.38
−91.4%
rush_hour_am
4.02
5.90
13.71
−31.8%
rush_hour_pm
0.07
2.49
1.76
−97.3%
holiday
0.35
5.73
3.39
−93.9%
incident
0.09
1.34
2.49
−93.5%
Mean Queue Length (halting vehicles / lane) at TL_A
Scenario
MAPPO
Fixed
MAPPO vs Fixed
low
0.01
0.04
−69.5%
normal
0.02
0.10
−75.3%
rush_hour_am
0.29
0.29
+2.1% ≈ same
rush_hour_pm
0.02
0.10
−84.1%
holiday
0.06
0.24
−75.9%
incident
0.02
0.06
−70.5%
Key Insights
• Waiting time: MAPPO reduces wait by 31.8% to 97.3% across ALL six scenarios
• rush_hour_am: queue is demand-bound (both controllers equal at 0.29) — but MAPPO still cuts wait by 31.8% and boosts throughput +20.9%
• holiday + incident: largest absolute wait reductions — MAPPO learns to hold empty phases and extend congested ones
• Two scenarios (normal, incident): MAPPO accepts ~10% less throughput to achieve 91–94% wait reduction — expected reward trade-off

## Slide 11
Evaluation Results — Throughput & Controller Comparison at TL_A
All metrics at TL_A; MAPPO on triple-intersection network, SPPO & Fixed on single-intersection network
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Total Throughput (vehicles crossing TL_A per episode)
Scenario
MAPPO
Fixed
MAPPO vs Fixed
low
13.67
13.67
0.0% (demand-limited)
normal
20.33
22.33
−9.0% (wait traded)
rush_hour_am
90.67
75.00
+20.9%
rush_hour_pm
13.67
12.33
+10.8%
holiday
81.67
64.33
+26.9%
incident
18.00
20.00
−10.0% (wait traded)
3-Controller Comparison at TL_A (per-step time-series)
Fixed-Time
Cycles A→B→C→D every 15 steps No queue awareness Baseline — worst overall
SPPO (SA-PPO)
PPO on single-intersection Local observation only Better than Fixed; cannot coordinate corridor
← Worse Better →
MAPPO
3 cooperative agents CTDE — global reward Best on all metrics except demand-limited cases
Performance hierarchy: MAPPO > SPPO > Fixed-Time
Per-step time-series at TL_A confirm consistently lower waiting times, queue lengths, stop ratios and pressures under MAPPO throughout the full 1800-second simulation.
Cross-Junction Behaviour (MAPPO only)
Green-wave coordination: TL_A releases platoon → TL_B/C widen receiving phase in step. Holiday: agents hold main-road phase longer (fewer phase switches). Incident: consolidates green on congested approach, drops empty-phase time.

## Slide 12
YOLOv8 Vehicle Detection Module
Camera-based sensing pipeline — validated on Palapye footage
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Why YOLOv8?
• Anchor-free detection head — better small-object recall, fewer hyperparameters
• Single-stage (one forward pass) — >100 FPS on mid-range GPU, suitable for real-time
• Instance-level bounding boxes — separate overlapping vehicles that fool blob detectors
• Trained on diverse lighting and weather conditions
• Outperforms classical OpenCV MOG2 on all criteria for outdoor intersection deployment
OpenCV MOG2 vs YOLOv8
Criterion
OpenCV MOG2
YOLOv8
Lighting robustness
Poor
Good
Occlusion handling
Poor
Good
Detection accuracy
~90% (cars)
>90% (all classes)
Queue estimation
Indirect
Direct (stationary bbox count)
Selected
No
YES
Current Status
• Module implemented and validated on sample Palapye traffic footage
• Queue length estimation: stationary bounding box count per approach arm
• Vehicle classes detected: car, truck, motorcycle, bus
• Independent validation only — not yet integrated into SUMO training loop
Future Integration Pathway
• Deploy calibrated camera at one A1 junction
• Validate queue estimates against manual counts (detection accuracy table)
• Replace SUMO TraCI observation with live YOLO estimates in MAPPO obs pipeline
• Closed-loop adaptive control: real camera → YOLO → MAPPO policy → signal actuation
Vision: real-world deployment replaces SUMO TraCI with live YOLOv8 observations

## Slide 13
Conclusions
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Phase 1: Single-Agent PPO Baseline
• Trained on one isolated SUMO junction; 9,000 timesteps, 5 demand phases
• 48.5% throughput improvement, 27.8% queue reduction, 27.3% pressure reduction vs Fixed (p < 0.001)
• Phase-specific: 50–68% delay improvement during peak/heavy demand
• Established quantitative benchmark for Phase 2 to surpass at network scale
Phase 2: MAPPO Multi-Intersection Extension
• All three A1 junctions controlled cooperatively; 1.5M steps; 6 demand scenarios; 3-stage curriculum
• Evaluation reward: 78% reduction in penalty over training; clean plateau at −2 confirms convergence
• At TL_A vs Fixed-Time: waiting time reduced 31.8–97.3% across all 6 scenarios
• Throughput: +10.8% to +26.9% in high-demand scenarios; small wait-vs-throughput trade-off under light demand
• Emergent cross-junction coordination: green wave progression, incident-adaptive phase consolidation
• First reported cooperative MARL evaluation on a Botswana signalised corridor
Phase 1 proved RL can learn adaptive signal control at a single junction. Phase 2 demonstrated cooperative MARL extends that capability to the full A1 corridor — delivering measurably stronger performance where single-agent and fixed-time approaches fail.

## Slide 14
Recommendations & Future Work
EEEN510 FYP | Tsotlhe Nayang Seiphepi | 21001137 | BIUST 2025
Field Traffic Count Collection
Obtain real turning movement counts from the Botswana Department of Roads to calibrate the SUMO model against actual demand.
Camera Calibration + YOLO Integration
Deploy calibrated camera at one A1 junction; validate queue estimates; integrate into the MAPPO observation pipeline for closed-loop control.
Actuated Baseline Comparison
Add a gap-based or Webster-optimised actuated controller as a more technically rigorous comparator beyond fixed-time.
Safety: Pedestrian Phases & Emergency Pre-emption
Add pedestrian crossing phases, minimum green guarantees, and emergency vehicle pre-emption to meet Botswana road safety standards.
Extended Training + Multi-Seed Evaluation
Scale to 5–10M steps with GPU acceleration; run multiple random seeds to quantify result variance and statistical robustness.
Emissions-Aware Reward
Incorporate fuel-consumption / idle-time penalty to align the control objective with Palapye air quality goals.
Hardware Deployment Roadmap
Define signal controller API, camera mounting specs, processing unit requirements, latency budget, and failsafe fallback to fixed-time.
Continual Learning Pipeline
Every live run generates timestep-level data; build a dataset pipeline that enables periodic fine-tuning from real-world observations.

## Slide 15
Thank You
Questions & Discussion
Tsotlhe Nayang Seiphepi | 21001137 | tsotlhenayangseiphepi@gmail.com Supervisor: Dr Bokamoso Basutli | BIUST | EEEN510 FYP 2025