## Slide 1
1
Adaptive Multi-Agent Reinforcement Learning for Traffic Signal Optimisation along the Palapye A1 Urban Corridor
SCHOOL OF ENGINEERING DEPARTMENT OF ELECTRICAL, COMPUTER AND TELECOMMUNICATIONS ENGINEERING EEEN510 Final Year Project Tsotlhe Nayang Seiphepi | 21001137 Supervisor: Dr Bokamoso Basutli Date: May 2025

## Slide 2
1
PRESENTATION OUTLINE
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
1. Introduction & Problem
2. Research Objectives
3. System Architecture
4. Phase 1 SA-PPO Results
5. MAPPO System Design
6. MAPPO Training
7. Evaluation Results
8. Conclusions & Recommendations
A two-phase project — from single-agent PPO at one junction to cooperative MAPPO across the full A1 Palapye corridor.

## Slide 3
2
INTRODUCTION & PROBLEM STATEMENT
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
• Palapye: key transit hub on the A1 highway between Gaborone and Francistown
• Morupule Coal Mine + BIUST campus drive recurrent, time-peaked demand
• Existing signals rely on static, pre-timed fixed cycles
• Fixed-time control is blind to queue lengths — cannot adapt to peak demand
• 3 closely spaced signalised junctions within ~1 km — decisions at one affect the others
• Consequences: chronic congestion, excessive idling, elevated emissions
PROBLEM STATEMENT
Urban intersections in Palapye experience chronic congestion due to fixed-time controllers that cannot adapt to real-time conditions, coordinate across junctions, or respond to varying demand.
RESEARCH GAP
• No adaptive/RL controller deployed or evaluated on a Botswana signalised network
• No publicly available traffic count dataset for Palapye intersections
This project builds and evaluates the first cooperative MARL traffic signal controller on a real Botswana road network.

## Slide 4
3
RESEARCH OBJECTIVES & CONTRIBUTIONS
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Four Objectives
• YOLOv8 vehicle detection module validated on Palapye traffic footage
• SUMO three-intersection A1 corridor model with 6 demand scenarios
• MAPPO with Centralised Training, Decentralised Execution (CTDE) for 3 cooperative agents
• Quantitative comparison: MAPPO vs SA-PPO vs Fixed-Time across all scenarios
Key Contributions
• First cooperative MARL controller on a real Botswana road network
• Reusable SUMO simulation environment (generates data for future researchers)
• First quantitative Fixed vs SA-PPO vs MAPPO comparison at the A1 corridor
• YOLOv8 pipeline providing a real-world sensing pathway
PHASE 1
Single-Agent PPO
1 junction • 1 demand scenario Stable-Baselines3 • ~5M steps
↓ extends to
PHASE 2
MAPPO CTDE
3 junctions • 6 scenarios • curriculum Custom MAPPO • 1.5M steps

## Slide 5
4
SYSTEM ARCHITECTURE
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Camera / YOLOv8
→
Traffic State Extraction
→
RL Policy Decision (PPO/MAPPO)
→
SUMO+TraCI Signal Actuation
→
Performance Metrics
↺ feedback loop: performance metrics drive next policy update
SUMO Network
Real Palapye A1 geometry 3 signalised junctions 6 demand scenarios Step: 3 s/action
MAPPO CTDE
22-dim local obs per agent 66-dim joint state for critic Global cooperative reward 3 agents, param sharing
YOLOv8
Anchor-free detection Validated on Palapye footage Queue length estimation Future: live integration

## Slide 6
5
PHASE 1: SINGLE-AGENT PPO vs FIXED-TIME
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Single intersection • 9,000 timesteps • 5 demand phases • Stable-Baselines3 PPO • ~5M training steps
Throughput
+48.5%
p<0.001 d=0.156
Queue Length
−27.8%
p<0.001 d=0.253
Traffic Pressure
−27.3%
p<0.001 d=0.239
Delay (agg.)
−10.1%
Negligible d=0.131
Stop Ratio
−3.6%
p=0.017 d=0.042
Delay aggregate is misleading — phase analysis shows 50–68% improvement during heavy/peak demand.
Demand Phase
Delay improv.
Queue improv.
Throughput improv.
Light (0–60 s)
+64.8%
—
—
Heavy (120–180 s)
+68.2%
+100%
+100%
Peak (180–240 s)
+50.1%
−34.4%
+—
Extended (300 s+)
−11.7%
+29.9%
+39.8%
These results confirmed RL can learn adaptive signal control — and established the baseline Phase 2 was designed to surpass at network scale.

## Slide 7
6
PHASE 2: MAPPO SYSTEM DESIGN — CTDE
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
WHY MAPPO?
• SA-PPO has no cross-junction visibility — cannot anticipate downstream spillback
• Fixed-time cycles blindly regardless of queue state
• MAPPO: each agent uses local 22-dim obs at execution time...
• ...but centralised critic sees full 66-dim joint state during training
• Global cooperative reward aligns all 3 agents to minimise network-wide waiting time
• Green wave pre-computation biases agents toward coordinated platoon release
Obs (22 dims): queue counts, wait time, stop ratio, phase one-hot, timer, green-wave offset
Action: Discrete(3) — 3 green phase configurations per junction
Local Obs o₁ Local Obs o₂ Local Obs o₃ (22-dim each)
↓
Shared Actor πθ (decentralised execution)
↓
Centralised Critic Vϕ (joint state 66-dim — training only)
3-Stage Curriculum
• Stage 1 — low + normal (establishes queue-clearing)
• Stage 2 — adds rush_hour_am/pm (phase extension)
• Stage 3 — all 6 scenarios incl. holiday + incident

## Slide 8
7
MAPPO TRAINING SETUP & DEMAND SCENARIOS
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Training Hyperparameters
Total timesteps
1,500,000
Parallel environments
4
Episode length
500 steps × 3 s = 25 min sim
PPO clip ε / GAE λ
0.2 / 0.95
Discount γ
0.99
Learning rate
3×10⁻⁴ (Adam)
Entropy coeff.
0.01
Hardware
Core i7 CPU, 16 GB RAM
Training time
~3–4 hours (CPU-only)
Reward: r = −Σ tanh(wait_i / (n_lanes · 60))
6 Demand Scenarios
low
Off-peak, minimal vehicles
normal
Average daily flow
rush_hour_am
Morning rush — inbound
rush_hour_pm
Evening rush — outbound
holiday
Heavy through-traffic, few turns
incident
Partial closure, asymmetric demand
Curriculum: Stage 1 (low+normal) → Stage 2 (+rush) → Stage 3 (all 6)
Network: Actor + Centralised Critic — 2 hidden layers × 128 units, tanh activations, orthogonal init

## Slide 9
8
MAPPO TRAINING CONVERGENCE
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Mean Training Reward
−15 → −9 over 1.5M steps Steep rise first 200k steps Plateaus near −9 from 1M+ Oscillations = multi-agent non-stationarity
Evaluation Reward (most important)
−9 → near −2 78% reduction in penalty Classic sigmoid learning curve Clean plateau beyond 1M steps Confirms stable cooperative policy
Centralised Critic Loss
Starts at ~4.5 (uninitialised) Drops sharply to ~1.5 Stabilises at 1.4–1.6 Prerequisite for reliable advantage estimation
Policy Entropy
0.95 → ~0.3 at convergence Near-uniform → confident Retains residual entropy Healthy MAPPO profile — not collapsed to zero
Actor Loss Arc
Begins near −0.004, rises to −0.002 mid-training (large gradients early on), then returns to −0.003 as PPO clipping activates less often. No spikes or sign changes — clipping prevented all destabilising updates.
Key takeaway: evaluation reward plateau at −2 vs −9 at start is the strongest evidence the agents reached a stable, generalisable cooperative policy.

## Slide 10
9
MAPPO EVALUATION — WAITING TIME & QUEUE LENGTH
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
All metrics at TL_A (junction 6073919354) • n=3 episodes per cell
Mean Waiting Time per Lane (s)
Scenario
MAPPO
Fixed
vs Fixed
low
0.06
0.97
−94.3%
normal
0.19
2.18
−91.4%
rush_hour_am
4.02
5.90
−31.8%
rush_hour_pm
0.07
2.49
−97.3%
holiday
0.35
5.73
−93.9%
incident
0.09
1.34
−93.5%
Mean Queue Length (halting veh / lane)
Scenario
MAPPO
Fixed
vs Fixed
low
0.01
0.04
−69.5%
normal
0.02
0.10
−75.3%
rush_hour_am
0.29
0.29
+2.1%
rush_hour_pm
0.02
0.10
−84.1%
holiday
0.06
0.24
−75.9%
incident
0.02
0.06
−70.5%
Key Insights
• Waiting time reduced 31.8%–97.3% across ALL six scenarios
• rush_hour_am: queue is demand-bound (both 0.29) — but MAPPO still cuts wait 31.8% and boosts throughput +20.9%
• holiday + incident: largest absolute wait reductions — MAPPO drops empty phases, extends congested ones

## Slide 11
10
EVALUATION — THROUGHPUT & CONTROLLER COMPARISON
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Total Throughput (vehicles crossing TL_A per episode)
Scenario
MAPPO
Fixed
vs Fixed
low
13.67
13.67
0.0% (demand-limited)
normal
20.33
22.33
−9.0% (wait traded)
rush_hour_am
90.67
75.00
+20.9%
rush_hour_pm
13.67
12.33
+10.8%
holiday
81.67
64.33
+26.9%
incident
18.00
20.00
−10.0% (wait traded)
FIXED-TIME
Pre-timed cycles No queue awareness Baseline — worst overall
SPPO (SA-PPO)
PPO on single junction Local obs only Better than Fixed; no corridor coordination
MAPPO
3 cooperative agents CTDE — global reward Best on all metrics (except demand-limited low)
Performance hierarchy: MAPPO > SPPO > Fixed-Time
Per-step time-series at TL_A confirm consistently lower waiting times, queues, stop ratios and pressures under MAPPO throughout the full 1,800-second simulation. MAPPO also exhibits emergent cross-junction coordination: green wave progression, incident-adaptive phase consolidation, holiday through-phase extension.

## Slide 12
11
YOLOV8 VEHICLE DETECTION MODULE
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
• Anchor-free detection head — better small-object recall, fewer hyperparameters
• Single-stage (one forward pass) — >100 FPS on mid-range GPU
• Instance-level bounding boxes — separates overlapping vehicles
• Outperforms classical OpenCV MOG2 on all criteria for outdoor intersections
• Validated on sample Palapye traffic footage (independent validation)
• Queue length estimated from stationary bounding-box count per approach arm
Criterion
OpenCV MOG2
YOLOv8
Lighting robustness
Poor
Good
Occlusion handling
Poor
Good
Detection accuracy
~90% cars
>90% all classes
Queue estimation
Indirect
Direct (stationary bbox)
Selected
No
YES
FUTURE INTEGRATION PATHWAY
• Deploy calibrated camera at one A1 junction
• Validate queue estimates vs manual counts
• Replace SUMO TraCI obs with live YOLO estimates in MAPPO obs pipeline
• Closed-loop: real camera → YOLO → MAPPO policy → signal actuation
Vision: real-world deployment replaces SUMO TraCI with live YOLOv8 observations
Current status: module implemented and validated independently; full integration with the SUMO training loop is identified as future work.

## Slide 13
12
CONCLUSIONS
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Phase 1: Single-Agent PPO Baseline
• Trained on one SUMO junction; 9,000 timesteps; 5 demand phases
• 48.5% throughput improvement, 27.8% queue reduction, 27.3% pressure reduction vs Fixed (p<0.001)
• 50–68% delay improvement during heavy/peak demand — aggregate figure misleading
• Established quantitative benchmark and proved RL can learn adaptive signal control
Phase 2: MAPPO Multi-Intersection Extension
• All 3 A1 junctions controlled cooperatively; 1.5M steps; 6 scenarios; 3-stage curriculum
• Evaluation reward: 78% reduction in penalty; clean convergence plateau confirmed
• Waiting time at TL_A vs Fixed: reduced 31.8%–97.3% across ALL 6 scenarios
• Throughput: +10.8% to +26.9% in high-demand; small trade-off under light demand
• Emergent cross-junction coordination: green wave, incident-adaptive phase consolidation
• First reported cooperative MARL evaluation on a Botswana signalised corridor
Phase 1 proved RL can learn adaptive signal control at one junction. Phase 2 demonstrated cooperative MARL extends that to the full A1 corridor — delivering measurably stronger performance where single-agent and fixed-time approaches fail.

## Slide 14
13
RECOMMENDATIONS & FUTURE WORK
INTRODUCTION
PROBLEM DEFINITION
PROJECT OBJECTIVES
METHODOLOGY
Field Traffic Count Collection
Obtain real turning movement counts from the Botswana DoR to calibrate the SUMO model.
Camera Calibration + YOLO Integration
Deploy at one A1 junction; validate queue estimates; integrate into MAPPO obs pipeline.
Actuated Baseline Comparison
Add Webster-optimised or gap-based actuated controller for rigorous benchmarking.
Safety: Pedestrian Phases + Emergency Pre-emption
Add pedestrian phases, min-green guarantees, emergency vehicle pre-emption.
Extended Training + Multi-Seed
Scale to 5–10M steps with GPU; run multiple seeds to quantify variance.
Emissions-Aware Reward
Incorporate idle-time fuel penalty to align objectives with Palapye air quality.
Hardware Deployment Roadmap
Define signal controller API, camera specs, latency budget, failsafe fallback.
Continual Learning Pipeline
Build dataset pipeline from live runs enabling periodic fine-tuning on real-world data.

## Slide 15
14
THANK YOU FOR YOUR TIME Tsotlhe Nayang Seiphepi | 21001137 tsotlhenayangseiphepi@gmail.com Supervisor: Dr Bokamoso Basutli | BIUST 2025 QnA
THANK YOU FOR YOUR TIME Tsotlhe Nayang Seiphepi | 21001137 tsotlhenayangseiphepi@gmail.com Supervisor: Dr Bokamoso Basutli | BIUST 2025 QnA